## Slide 2: Drone
Definition: an unmanned aircraft system; remote-controlled pilot-less aircraft; flying thingy without people inside controlling it;
The FAA calls them Unmanned Aircraft Systems (UAS), but no one will argue if you call them a drone

## Slide 3: Why Fly Drones?
Aerial photography
Digital archeology
Environmental analysis
Agricultural analysis
Gas mapping
Coastal surveys
Film/media
Law enforcement
Drone racing/ first person view

## Slide 4: Where Did the Term “Drone” come from?

## Slide 5: The Queen Bee (DH.82B)
Gipsy Moth, one of the most common aircrafts in UK in 1929
1935 - Put radio controls on a de Havilland Tiger Moth, a successor to the Gipsy Moth
The Queen Bee (DH.82B) was one of the first returnable and reusable UAV - used as practice targets.
Aircrafts have commonly been named after insects

## Slide 6: TDD-1 – Target Drone Denny 1
Reginald Denny career as actor and radio control model aircrafts
Contract signed with the Navy was for TDD-1
The first instance of “Drone” being associated with remotely piloted vehicle

## Slide 7: What are Some Other Names of Drones?
Quadcopter
Multicopter
Hexicopter
Octorotor
Hexarotor
Unmanned Aircraft Vehicle - UAV
Unmanned Aerial System – UAS
Internationally known as Remotely Piloted Aircraft Systems (RPAS)
UAS is the correct nomenclature for the FAA

## Slide 8: Classification of Drones

## Slide 9: Classification Diagram
Laws that affect aircrafts affect Model Aircrafts and Unmanned Aircrafts
Laws that affect Unmanned Aircrafts also affect Model Aircrafts

## Slide 10: Classification of Drones
Drones classified by weight
  Small Unmanned Aircraft System < 55 lbs
  “micro” < 4.4 lbs
Model Aircrafts classified by the purpose of only recreational
  Drone racing drones classified by size

## Slide 11: How Long do Drones Fly?
Chart: Average Flight Time
| Solo | IRIS+ | DJI Phantom 3 | DJI Phantom 4 | SenseFly eBee | Sirius Pro
Column1
Series 2 | 20 | 20 | 25 | 28 | 45 | 50
Column2
Time (Minutes)

## Slide 12: Flying UAS

## Slide 13: What Permissions are Needed to Legally Fly?
Federal Aviation Administration (FAA) - must register vehicle with FAA and have authorization to fly
Section 333 – any aircraft operation in national airspace requires a certificated and registered aircraft, a licensed pilot, and operational approval
Certificate of Waiver or Authorization (COA) - authorization by Air Traffic Organization for specific UA activity
Part 107 - simplifies current laws, announced JUNE 2016

## Slide 14: What Items Do You Need To Legally Fly?
Recreational
  License number registered with FAA displayed on aircrafts
  Registration fee $5 per person
Commercial
  Section 333 Exception or Aircraft Certification
  Certificate of Authorization (COA)
  Aircraft Registrations and Markings
  Pilot Certificate
  Registration $5 per aircraft
  Maybe, Certificate of Authorization (COA)

## Slide 15: Recreational/Class Curriculum
Recreational
Cannot receive money or compensation
Cannot be used in furtherance with a business or official duty
Must be operated within a community-based set of safety guidelines and within the programming of a nationwide community-based organization
Education
Students may build and fly a UAS as a component of a course curriculum or senior project
UAS flights by students must be in accordance with Campus oversight.
UAS flights in pursuit of research projects or university business are not considered recreational

## Slide 16: UC User Flight Workflow
Flight Request
To Center
(UC form)
File special permission with FAA
Clear Airspace?
Where:
When:
Purpose:
Pilot:
Aircraft:
Aircraft Registered?
Licensed Pilot
File NOTAM (online system)
Flight Authorized
Flight Report
(UC form)
Flight!
UC UAS Fleet Management System under development!

## Slide 17: Where can we fly?

## Slide 18: Where is it legal to fly? Where is it safe to fly?
Legal
Class G airspace
Under 400 ft altitude
Within Line of Sight
Outside of 5 NM of an airport
Other locations will require additional FAA authorization
Safe
No flying over non-participants
Area should be secured or very likely to have no incursions
Spectators should be
  65 ft away for planes
  25 ft away for multirotors (quadrotors)

## Slide 19: Airspace Classifications

## Slide 20: RDU Airspace
RDU is Class C
Duke and UNC have helipads
Stadiums
UNC Special Case

## Slide 22: Mapping Solutions
Skyvector.com
App.airmap.io

## Slide 23: Quadcopter Anatomy
Physical
  Rotors
  Motors
  Props
  Frame
  Landing Struts
Electronic
  GPS Receiver
  RF Receiver
  Transmitter
  Flight Controller
Optional
  Gimbal
  FPV Camera

## Slide 24: How to Operate a Drone

## Slide 25: How to Operate a Drone
Visual Observer
Pilot in Command
Ground Control Station
Crew Member
Control & Communication Link
RC & Safety Link
PIC – Pilot in Command
Ground Control Station (GCS)
Visual Observer (VO)
Radio
Safety Link / RC Communication
Control & Communication (C2)
Notes: Make a visual image showing all the items

## Slide 26: UAS Operation
A. Pilot in Command
B. Ground Control Station
The person ultimately responsible for the safety an operation of the aircraft during the flight
Abbreviated PIC
Provides the facilities and computers for human control of UAV
Abbreviated GCS

## Slide 27: UAS Operation
C. Visual Observer
Secondary person to watch the sky for intruding aircrafts and watch the unmanned aircraft
  Common practice to have a visual observer
Abbreviated VO

## Slide 28: UAS Operation
Control & Communication RC Link

## Slide 29: UAS Operation
E. Control & Communication
Flight controller used for control
Communication between flight controller and ground station typically done by radio
Abbreviated C2
F. Safety Link & RC Communication
Safety Link typically RC transmitter link
Could also be a different process, such as
  Radio signal
  Digital wifi
  Linked to RC Communication

## Slide 30: Drone Rotational Motion
Roll- rotation along the y axis
Pitch- rotation about the x axis
Yaw- rotation about the z axis

## Slide 31: What Can Go Wrong?

## Slide 32: Things That Go Wrong
Pilot Error!
Too windy
Loss of communication
Fly-away – Automated system error
Loss of GPS
Loss of Altitude (IMU failure)

## Slide 33: Getting Trained
Register for RemotePilot101.com
  Finish Sections 1 and 2 by next week.
  You need to average 2.5 Sections per week to be done before Spring Break.
In-Field Drone Training
  Arrive at Ranbow Soccer Field by 2:30pm
  Cleland Rd, Chapel Hill, NC 27517

## Slide 34: Appendix: Common UAS Key Terms (Marketing terms, special features, add-ons)

## Slide 35: UAS Operations Key Terms
A. Autonomous
B. Altitude Hold Function
acting independently; without human control
UAV maintained at consistent altitude while roll, pitch, and yaw still changeable

## Slide 36: UAS Operations Key Terms
C. Return to Home
D. Waypoint Navigation
Function used to sent the UAV back to the takeoff position
UAV flies to GPS points

## Slide 37: UAS Operations Key Terms
E. Manual Control
F. Payload
Flies by Not Waypoint Navigation
Someone is controlling the direct motion
Equipment being carried, such as:
  Camera
  Air measurements
  Lasers
  And so on

## Slide 38: UAS Operations Key Terms
H. Fly-Away Protection
G. Geofence
GPS tells drone to never go outside the GPS range
Marketing Term used for
  Geofencing
  Autolanding

## Slide 39: UAS Operations Key Terms
I. Intelligent Orientation Control
J. Sense and Avoid
The forward direction of the UAV is the same as the recorded nose direction, “home point”
UAV uses sensors to maneuver around obstacles and avoid collision, can use:
  Cameras
  Ultrasonic sensors
  Lasers

## Slide 40: UAS Operations Key Terms
K. Visual Tracking
L. Fail-Safe
Using cameras to control the roll, pitch, and yaw to track a moving object
Prevents crash in the event of unsafe situation, such as:
  Loss of GPS signal
  Loss of Radio Control Signal
  Low Battery

## Slide 41: UAS Operations Key Terms
M. Arming
N. Ultrasonic Sensors
Armed aircraft is ready to fly and motors will spin when throttle is applied
Used as a safety mechanism
Equipment used for range measurements by sending and receiving a signal
Example:
  Bats
  Drone collision avoidance

## Slide 42: UAS Operations Key Terms
O. Optical Flow
P. Above Ground Level
Used to improve stability using a camera to detect the direction of motion
Indicates where the zero level or reference altitude is located
Abbreviated AGL

## Slide 43: UAS Operations Key Terms
Q. First Person View
Drone racing
Watch video it’s fun

## Slide 44: UAS Operations Key Terms
R. Line of Sight
S. Beyond Line of Sight
Straight line along which the observer has unobstructed view
Abbreviated LOS
Operator and UAV too distant or obstructed
Abbreviated BLOS

## Slide 45: UAS Operations Key Terms
T. No Fly Zone
U. Notice to Airman
Designated area where aircrafts may not fly
Abbreviated NFZ
Notice filed to aviation authority to notify aircraft pilots of:
  potential hazards along flight route
  locations associated with the flight
Abbreviated NOTAM

## Slide 46: UAS Operations Key Terms
V. Air Traffic Control
W. National Airspace System
Directs aircraft traffic through controlled airspace
Abbreviated ATC
Airspace, navigation facilities and airports of the United States along with their rules and regulations
Abbreviated NAS

## Slide 47: UAS Operations Key Terms
X. Total Flight Restriction
Occurs when the FAA shuts down airspace
Announced by FAA
Cannot be requested
Can occur at times of
  Large stadium events
  President arriving in a city
  And so forth